------------------------------------------------------------------------------

  K-Meter
  =======
  Implementation of a K-System meter according to Bob Katz' specifications

  Copyright (c) 2010-2015 Martin Zuther (http://www.mzuther.de/)

  This program is free software: you can redistribute it and/or modify
  it under the terms of the GNU General Public License as published by
  the Free Software Foundation, either version 3 of the License, or
  (at your option) any later version.

  This program is distributed in the hope that it will be useful,
  but WITHOUT ANY WARRANTY; without even the implied warranty of
  MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the
  GNU General Public License for more details.

  You should have received a copy of the GNU General Public License
  along with this program. If not, see <http://www.gnu.org/licenses/>.

  Thank you for using free software!

------------------------------------------------------------------------------

FLAC-compressed wave file (44.1 kHz, 16 bit, stereo)
====================================================
Please verify correctness of meter ballistics programmatically. Calculated values are only valid in “RMS” mode. Small differences due to time granularity of validation logging are acceptable.

00:00.000 - 00:02.000 silence
00:02.000 - 00:12.000 sine wave (2 kHz, 0.0 dB FS peak)
00:12.000 - 00:12.600 silence

00:12.600 [check fall time of average meters]

00:12.600 - 00:14.600 sine wave (2 kHz, 0.0 dB FS peak)
00:14.600 - 00:24.600 silence
00:24.600 - 00:25.200 sine wave (2 kHz, 0.0 dB FS peak)

00:25.200 [check rise time of average meters]

00:25.200 - 00:27.200 silence
00:27.200 - 00:37.200 sine wave (2 kHz, 0.0 dB FS peak)
00:37.200 - 00:40.200 silence

00:40.200 [check fall/rise time of peak meters]

00:40.200 - 00:42.200 sine wave (2 kHz, 0.0 dB FS peak)
00:42.200 - 00:44.200 silence
Validation settings
===================
File: meter_ballistics.flac
Host SR: 44 100 Hz
Channel: RMS: All, ITU-R: 1
Display: [x] Peak meter level
        [x] Average meter level
        [ ] Maximum peak level
        [ ] Stereo meter value
        [ ] Phase correlation

Metering minima
===============
-90.01 dB (see “MeterBallistics::fMeterMinimumDecibel”)

Fall time of average meters (sine wave, 0.0 dB FS peak)
=======================================================
99% of final reading in 600 ms integration time

K-20 = 20.00 dB - 90.01 dB * 99% = -69.11 dB (ITU-R: -66.8 dB)
K-14 = 14.00 dB - 90.01 dB * 99% = -75.11 dB (ITU-R: -72.8 dB)
K-12 = 12.00 dB - 90.01 dB * 99% = -77.11 dB (ITU-R: -74.8 dB)
Norm = 0.00 dB - 90.01 dB * 99% = -89.11 dB (ITU-R: -86.8 dB)

Rise time of average meters (sine wave, 0.0 dB FS peak)
=======================================================
99% of final reading in 600 ms integration time

K-20 = 20.00 dB - 90.01 dB * 1% = 19.10 dB (ITU-R: 21.4 dB)
K-14 = 14.00 dB - 90.01 dB * 1% = 13.10 dB (ITU-R: 15.4 dB)
K-12 = 12.00 dB - 90.01 dB * 1% = 11.10 dB (ITU-R: 13.4 dB)
Norm = 0.00 dB - 90.01 dB * 1% = -0.90 dB (ITU-R: 1.4 dB)

Fall time of peak meters (sine wave, 0.0 dB FS peak)
====================================================
-26 dB in 3 seconds

K-20 = 20.00 dB - 26.00 dB = -6.00 dB
K-14 = 14.00 dB - 26.00 dB = -12.00 dB
K-12 = 12.00 dB - 26.00 dB = -14.00 dB
Norm = 0.00 dB - 26.00 dB = -26.00 dB

Rise time of peak meters (sine wave, 0.0 dB FS peak)
====================================================
immediate (one sample)

K-20 = 20.00 dB
K-14 = 14.00 dB
K-12 = 12.00 dB
Norm = 0.00 dB