------------------------------------------------------------------------------

  K-Meter
  =======
  Implementation of a K-System meter according to Bob Katz' specifications

  Copyright (c) 2010-2015 Martin Zuther (http://www.mzuther.de/)

  This program is free software: you can redistribute it and/or modify
  it under the terms of the GNU General Public License as published by
  the Free Software Foundation, either version 3 of the License, or
  (at your option) any later version.

  This program is distributed in the hope that it will be useful,
  but WITHOUT ANY WARRANTY; without even the implied warranty of
  MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the
  GNU General Public License for more details.

  You should have received a copy of the GNU General Public License
  along with this program. If not, see <http://www.gnu.org/licenses/>.

  Thank you for using free software!

------------------------------------------------------------------------------

FLAC-compressed wave file (44.1 kHz, 24 bit, stereo)
====================================================
Please verify correctness of peak meter and maximum peak meter programmatically. In “ITU-R BS.1770” mode, make sure that measured levels equal the left channel's level.

Given levels describe the left channel. The left channel is delayed by one second, while the right channel's level has been attenuated by 1.93 dB.

00:00.000 - 00:02.000 silence
00:02.000 - 00:07.000 square wave ( 20 Hz, -41.0 dB FS peak)

        [left peak meter should read -21.00 dB (K-20)]
        [right peak meter should read -22.93 dB (K-20)]

        [left maximum peak should read -21.00 dB (K-20)]
        [right maximum peak should read -22.93 dB (K-20)]

00:07.000 - 00:09.000 silence
00:09.000 - 00:14.000 square wave ( 180 Hz, -29.0 dB FS peak)

        [left peak meter should read -9.00 dB (K-20)]
        [right peak meter should read -10.93 dB (K-20)]

        [left maximum peak should read -9.00 dB (K-20)]
        [right maximum peak should read -10.93 dB (K-20)]

00:14.000 - 00:16.000 silence
00:16.000 - 00:21.000 square wave ( 530 Hz, -17.5 dB FS peak)

        [left peak meter should read +2.50 dB (K-20)]
        [right peak meter should read +0.57 dB (K-20)]

        [left maximum peak should read +2.50 dB (K-20)]
        [right maximum peak should read +0.57 dB (K-20)]

00:21.000 - 00:23.000 silence
00:23.000 - 00:28.000 square wave (1111 Hz, -8.3 dB FS peak)

        [left peak meter should read +11.70 dB (K-20)]
        [right peak meter should read +9.77 dB (K-20)]

        [left maximum peak should read +11.70 dB (K-20)]
        [right maximum peak should read +9.77 dB (K-20)]

00:28.000 - 00:30.000 silence
00:30.000 - 00:35.000 square wave (1501 Hz, -0.1 dB FS peak)

        [left peak meter should read +19.90 dB (K-20)]
        [right peak meter should read +17.97 dB (K-20)]

        [left maximum peak should read +19.90 dB (K-20)]
        [right maximum peak should read +17.97 dB (K-20)]

00:35.000 - 00:37.000 silence
00:37.000 - 00:42.000 square wave (2890 Hz, -36.0 dB FS peak)

        [left peak meter should read -16.00 dB (K-20)]
        [right peak meter should read -17.93 dB (K-20)]

        [left maximum peak should read +19.90 dB (K-20)]
        [right maximum peak should read +17.97 dB (K-20)]

00:42.000 - 00:44.000 silence
00:44.000 - 00:49.000 square wave (4190 Hz, -69.5 dB FS peak)

        [left peak meter should read -49.50 dB (K-20)]
        [right peak meter should read -51.43 dB (K-20)]

        [left maximum peak should read +19.90 dB (K-20)]
        [right maximum peak should read +17.97 dB (K-20)]

00:49.000 - 00:51.000 silence
00:51.000 - 00:56.000 square wave (8345 Hz, -85.0 dB FS peak)

        (it seems like I have driven Sound Forge's test
        tone generator to its limits -- the peak level
        meter readings given below have been measured
        using the "Statistics" dialog in Sound Forge)

        [left peak meter should read -65.05 dB (K-20)]
        [right peak meter should read -66.99 dB (K-20)]

        [left maximum peak should read +19.90 dB (K-20)]
        [right maximum peak should read +17.97 dB (K-20)]

00:56.000 - 00:59.000 silence

Validation settings
===================
File: peak_meter.flac
Host SR: 44 100 Hz
Channel: RMS: All, ITU-R: 1
Display: [x] Peak meter level
        [ ] Average meter level
        [x] Maximum peak level
        [ ] Stereo meter value
        [ ] Phase correlation