------------------------------------------------------------------------------

  K-Meter
  =======
  Implementation of a K-System meter according to Bob Katz' specifications

  Copyright (c) 2010-2012 Martin Zuther (http://www.mzuther.de/)

  This program is free software: you can redistribute it and/or modify
  it under the terms of the GNU General Public License as published by
  the Free Software Foundation, either version 3 of the License, or
  (at your option) any later version.

  This program is distributed in the hope that it will be useful,
  but WITHOUT ANY WARRANTY; without even the implied warranty of
  MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the
  GNU General Public License for more details.

  You should have received a copy of the GNU General Public License
  along with this program. If not, see <http://www.gnu.org/licenses/>.

  Thank you for using free software!

------------------------------------------------------------------------------

FLAC-compressed wave file (44.1 kHz, 16 bit, stereo)
====================================================
Please verify readout of stereo meter programmatically.

00:00.000 - 00:02.000 silence

00:02.000 - 00:05.000 sine waves (1 kHz)
        left channel: -12.00 dB FS peak (100 %)
        right channel: muted ( 0 %)

        [stereo meter should read -1.00]

00:05.000 - 00:07.000 silence

00:07.000 - 00:10.000 sine waves (1 kHz)
        left channel: -12.00 dB FS peak (100 %)
        right channel: -18.02 dB FS peak ( 50 %)

        [stereo meter should read -0.50]

00:10.000 - 00:12.000 silence

00:12.000 - 00:15.000 sine waves (1 kHz)
        left channel: -12.00 dB FS peak (100 %)
        right channel: -12.00 dB FS peak (100 %)

        [stereo meter should read 0.00]

00:15.000 - 00:17.000 silence

00:17.000 - 00:20.000 sine waves (1 kHz)
        left channel: -18.02 dB FS peak ( 50 %)
        right channel: -12.00 dB FS peak (100 %)

        [stereo meter should read +0.50]

00:20.000 - 00:22.000 silence

00:22.000 - 00:25.000 sine waves (1 kHz)
        left channel: muted ( 0 %)
        right channel: -12.00 dB FS peak (100 %)

        [stereo meter should read +1.00]

00:25.000 - 00:27.000 silence

Validation settings
===================
File: stereo_meter.flac
Host SR: 44 100 Hz
Channel: All
Display: [ ] Average meter level
        [ ] Peak meter level
        [ ] Maximum peak level
        [x] Stereo meter value
        [ ] Phase correlation