------------------------------------------------------------------------------

  K-Meter
  =======
  Implementation of a K-System meter according to Bob Katz' specifications

  Copyright (c) 2010-2013 Martin Zuther (http://www.mzuther.de/)

  This program is free software: you can redistribute it and/or modify
  it under the terms of the GNU General Public License as published by
  the Free Software Foundation, either version 3 of the License, or
  (at your option) any later version.

  This program is distributed in the hope that it will be useful,
  but WITHOUT ANY WARRANTY; without even the implied warranty of
  MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the
  GNU General Public License for more details.

  You should have received a copy of the GNU General Public License
  along with this program. If not, see <http://www.gnu.org/licenses/>.

  Thank you for using free software!

------------------------------------------------------------------------------

FLAC-compressed wave file (44.1 kHz, 16 bit, stereo)
====================================================
Please verify phase correlation meter programmatically.

00:00.000 - 00:02.000 silence

00:02.000 - 00:22.000 two triangular waves (linear phase sweep)
        left channel: 441.0 Hz, -12 dB FS peak
        right channel: 441.1 Hz, -12 dB FS peak

        [phase correlation meter should oscillate twice
        from approximately +1.00 to -1.00 and back]

00:22.000 - 00:24.000 silence

00:24.000 - 00:27.000 two triangular waves (441 Hz, -12 dB FS peak)
        left channel: 0 samples delay
        right channel: 0 samples delay

        [phase correlation meter should read +1.00]

00:27.000 - 00:29.000 silence

00:29.000 - 00:32.000 two triangular waves (441 Hz, -12 dB FS peak)
        left channel: 0 samples delay
        right channel: 10 samples delay

        [phase correlation meter should read +0.79]

00:32.000 - 00:34.000 silence

00:34.000 - 00:37.000 two triangular waves (441 Hz, -12 dB FS peak)
        left channel: 0 samples delay
        right channel: 20 samples delay

        [phase correlation meter should read +0.30]
00:37.000 - 00:39.000 silence

00:39.000 - 00:42.000 two triangular waves (441 Hz, -12 dB FS peak)
        left channel: 0 samples delay
        right channel: 30 samples delay

        [phase correlation meter should read -0.30]

00:42.000 - 00:44.000 silence

00:44.000 - 00:47.000 two triangular waves (441 Hz, -12 dB FS peak)
        left channel: 0 samples delay
        right channel: 40 samples delay

        [phase correlation meter should read -0.79]

00:47.000 - 00:49.000 silence

00:49.000 - 00:52.000 two triangular waves (441 Hz, -12 dB FS peak)
        left channel: 0 samples delay
        right channel: 50 samples delay

        [phase correlation meter should read -1.00]

00:52.000 - 00:54.000 silence

Validation settings
===================
File: phase_correlation_meter.flac
Host SR: 44 100 Hz
Channel: All
Display: [ ] Average meter level
        [ ] Peak meter level
        [ ] Maximum peak level
        [ ] Stereo meter value
        [x] Phase correlation

Linear phase sweep
==================
left channel: (441.0 periods / second) * 20 seconds = 8820 periods
right channel: (441.1 periods / second) * 20 seconds = 8822 periods
        ------------
difference: 2 periods

--> phase correlation oscillates *twice* between +1 and -1 (but keep
    in mind that meter ballistics interfere with the sweep and thus
    lead to a range of approximately +0.98 to -0.98)

--> please keep in mind that while the phase sweep is linear, the
    corresponding phase correlation is *not* linear (see below)!
Static phase shift
==================
Phase correlation has been calculated using the cross-correlation
function "ccf" in R (see "phase_correlation_meter.R" in this folder).

period length = (44100 samples / second) / 441 Hz = 100 samples

  0 samples delay / 100 samples = 0 % phase offset
--> phase correlation: +1.00

 10 samples delay / 100 samples = 10 % phase offset
--> phase correlation: +0.79

 20 samples delay / 100 samples = 20 % phase offset
--> phase correlation: +0.30

 30 samples delay / 100 samples = 30 % phase offset
--> phase correlation: -0.30

 40 samples delay / 100 samples = 40 % phase offset
--> phase correlation: -0.79

 50 samples delay / 100 samples = 50 % phase offset
--> phase correlation: -1.00