------------------------------------------------------------------------------

  K-Meter
  =======
  Implementation of a K-System meter according to Bob Katz' specifications

  Copyright (c) 2010-2013 Martin Zuther (http://www.mzuther.de/)

  This program is free software: you can redistribute it and/or modify
  it under the terms of the GNU General Public License as published by
  the Free Software Foundation, either version 3 of the License, or
  (at your option) any later version.

  This program is distributed in the hope that it will be useful,
  but WITHOUT ANY WARRANTY; without even the implied warranty of
  MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the
  GNU General Public License for more details.

  You should have received a copy of the GNU General Public License
  along with this program. If not, see <http://www.gnu.org/licenses/>.

  Thank you for using free software!

------------------------------------------------------------------------------

FLAC-compressed wave file (96 kHz, 24 bit, stereo)
==================================================
Please verify correctness of K-System meter values programmatically. In “RMS mode”, make sure that peak and average readouts match for sine waves.

Please notice that K-System meter readings may deviate from the true value at very low frequencies (fluctuations due to meter ballistics and audio chunk size) and very high frequencies (aliasing in the wave file).

00:00 - 00:03 silence
00:03 - 01:03 sine sweep (10 Hz to 48 kHz, -4.00 dB FS peak, logarithmic)

        [check peak and average meter, see below]
00:57 [check peak meter for RMS filter cutoff @21 kHz]

01:03 - 01:06 silence
01:06 - 01:26 sine sweep (20 kHz to 24 kHz, -4.00 dB FS peak, linear)

        [check peak and average meter, see below]
01:11 [check peak meter for RMS filter cutoff @21 kHz]

01:26 - 01:29 silence
01:29 - 01:49 triangular sweep (20 Hz to 20 kHz, -4.00 dB FS peak, logarithmic)

        [check peak and average meter, see below]

01:49 - 01:52 silence
01:52 - 02:12 square sweep (20 Hz to 20 kHz, -4.00 dB FS peak, logarithmic)

        [check peak and average meter, see below]

02:12 - 02:15 silence
Validation settings
===================
File: rms_sweeps.flac
Host SR: 96 000 Hz
Channel: All
Display: [x] Average meter level
        [x] Peak meter level
        [ ] Maximum peak level
        [ ] Stereo meter value
        [ ] Phase correlation

RMS correction of K-System meter (sine wave, -4.00 dB FS peak)
==============================================================
RMS = A / sqrt(2)
RMS / A = sqrt(2) = +3.01 dB
+3.01 dB + (-4.00 dB) = -0.99 dB

K-20 = 20.00 dB + (-0.99 dB) = 19.01 dB
K-14 = 14.00 dB + (-0.99 dB) = 13.01 dB
K-12 = 12.00 dB + (-0.99 dB) = 11.01 dB
Norm = 0.00 dB + (-0.99 dB) = -0.99 dB

Sine wave (-4.00 dB FS peak)
============================
RMS = A / sqrt(2)
A / RMS = 1/sqrt(2) = -3.01 dB

K-20 = 19.01 dB + (-3.01 dB) = 16.00 dB
K-14 = 13.01 dB + (-3.01 dB) = 10.00 dB
K-12 = 11.01 dB + (-3.01 dB) = 8.00 dB
Norm = -0.99 dB + (-3.01 dB) = -4.00 dB

Triangular or sawtooth wave (-4.00 dB FS peak)
==============================================
RMS = A / sqrt(3)
A / RMS = 1/sqrt(3) = -4.77 dB

K-20 = 19.01 dB + (-4.77 dB) = 14.24 dB
K-14 = 13.01 dB + (-4.77 dB) = 8.24 dB
K-12 = 11.01 dB + (-4.77 dB) = 6.24 dB
Norm = -0.99 dB + (-4.77 dB) = -5.76 dB

Square wave (-4.00 dB FS peak)
==============================
RMS = A
A / RMS = 1 = 0.00 dB

K-20 = 19.01 dB + ( 0.00 dB) = 19.01 dB
K-14 = 13.01 dB + ( 0.00 dB) = 13.01 dB
K-12 = 11.01 dB + ( 0.00 dB) = 11.01 dB
Norm = -0.99 dB + ( 0.00 dB) = -0.99 dB