------------------------------------------------------------------------------

  K-Meter
  =======
  Implementation of a K-System meter according to Bob Katz' specifications

  Copyright (c) 2010-2011 Martin Zuther (http://www.mzuther.de/)

  This program is free software: you can redistribute it and/or modify
  it under the terms of the GNU General Public License as published by
  the Free Software Foundation, either version 3 of the License, or
  (at your option) any later version.

  This program is distributed in the hope that it will be useful,
  but WITHOUT ANY WARRANTY; without even the implied warranty of
  MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the
  GNU General Public License for more details.

  You should have received a copy of the GNU General Public License
  along with this program. If not, see <http://www.gnu.org/licenses/>.

  Thank you for using free software!

------------------------------------------------------------------------------

FLAC-compressed wave file (44.1 kHz, 16 bit)
============================================
Please verify readout of overflow counter by making use of your eyes
and ears.

Given values describe the left channel. The right channel is delayed
by one second and contains a sine wave with a frequency of 500 Hz.

00:00.000 - 00:02.000 silence

00:02.000 - 00:05.000 sine wave (150 Hz, -5.5 dBFS)

        [both channels: first audible click must not register]
        [both channels: second audible click must register]

        [left channel: a total of 16 clips must register]
        [right channel: a total of 9 clips must register]

00:05.000 - 00:07.000 silence

Validation settings
===================
File: overflow.flac
Host SR: 44 100 Hz
Channel: All
Display: [ ] Average meter level
        [ ] Peak meter level
        [ ] Maximum peak level
        [ ] Stereo meter value
        [ ] Phase correlation

Samples reaching digital full scale
===================================
both channels: 1 sample of integer level 32'764
        1 adjoining negated sample of integer level 32'764

        --> these peaks MUST NOT register

both channels: 1 sample of integer level 32'765
        1 adjoining negated sample of integer level 32'765

        --> these peaks MUST register

left channel: 4 continuous positive samples

left channel: 2 continuous negative samples

left channel: 1 positive sample
        1 adjoining negative sample

left channel: 2 continuous positive samples
        1 "valid" sample
        2 continuous negative samples

right channel: 1 positive sample

right channel: 1 negative sample
        1 adjoining positive sample

left channel: 1 negative sample

left channel: 1 positive sample

right channel: 2 continuous negative samples
        1 "valid" sample
        2 continuous positive samples