------------------------------------------------------------------------------

  This documentation by Martin Zuther is licensed under a Creative Commons
  Attribution-ShareAlike 4.0 International License. The accompanying audio
  file is used with permission by Bob Katz.

------------------------------------------------------------------------------

FLAC-compressed wave file (44.1 kHz, 16 bit, stereo)
====================================================
Stereo uncorrelated pink noise (-20 dBFS RMS, band-limited to 20 Hz -- 20 kHz). This file has been downloaded from http://www.digido.com (original file name Pink_min_20_dBFS_RMS_uncor_st_441.WAV).

Please verify correctness of the average meter programmatically (0 dB on the K-20 scale in RMS mode).

00:00.000 - 00:15.000 -20 dBFS RMS uncorrelated pink noise

Validation settings
===================
File: pink_noise_bandlimited.flac
Host SR: 44 100 Hz
Channel: All
Display: [ ] Peak meter level
        [x] Average meter level
        [ ] Maximum peak level
        [ ] Stereo meter value
        [ ] Phase correlation