------------------------------------------------------------------------------

  This documentation and its accompanying audio file by Martin Zuther are
  licensed under a Creative Commons Attribution-ShareAlike 4.0 International
  License.

------------------------------------------------------------------------------

FLAC-compressed wave file (44.1 kHz, 16 bit, stereo)
====================================================
Please verify readout of stereo meter programmatically.

00:00.000 - 00:02.000 silence

00:02.000 - 00:05.000 sine waves (1 kHz)
        left channel: -12.00 dB FS peak (100 %)
        right channel: muted ( 0 %)

        [stereo meter should read -1.00]

00:05.000 - 00:07.000 silence

00:07.000 - 00:10.000 sine waves (1 kHz)
        left channel: -12.00 dB FS peak (100 %)
        right channel: -18.02 dB FS peak ( 50 %)

        [stereo meter should read -0.50]

00:10.000 - 00:12.000 silence

00:12.000 - 00:15.000 sine waves (1 kHz)
        left channel: -12.00 dB FS peak (100 %)
        right channel: -12.00 dB FS peak (100 %)

        [stereo meter should read 0.00]

00:15.000 - 00:17.000 silence

00:17.000 - 00:20.000 sine waves (1 kHz)
        left channel: -18.02 dB FS peak ( 50 %)
        right channel: -12.00 dB FS peak (100 %)

        [stereo meter should read +0.50]

00:20.000 - 00:22.000 silence

00:22.000 - 00:25.000 sine waves (1 kHz)
        left channel: muted ( 0 %)
        right channel: -12.00 dB FS peak (100 %)

        [stereo meter should read +1.00]

00:25.000 - 00:27.000 silence
Validation settings
===================
File: stereo_meter.flac
Host SR: 44 100 Hz
Channel: All
Display: [ ] Peak meter level
        [ ] Average meter level
        [ ] Maximum peak level
        [x] Stereo meter value
        [ ] Phase correlation