------------------------------------------------------------------------------

  This documentation and its accompanying audio file by Martin Zuther are
  licensed under a Creative Commons Attribution-ShareAlike 4.0 International
  License.

------------------------------------------------------------------------------

FLAC-compressed wave file (44.1 kHz, 16 bit, stereo)
====================================================
Please verify correctness of meter ballistics programmatically. Calculated values are only valid in “RMS” mode. Small differences due to time granularity of validation logging are acceptable.

00:00.000 - 00:02.000 silence
00:02.000 - 00:12.000 sine wave (2 kHz, 0.0 dB FS peak)
00:12.000 - 00:12.600 silence

00:12.600 [check fall time of average meters]

00:12.600 - 00:14.600 sine wave (2 kHz, 0.0 dB FS peak)
00:14.600 - 00:24.600 silence
00:24.600 - 00:25.200 sine wave (2 kHz, 0.0 dB FS peak)

00:25.200 [check rise time of average meters]

00:25.200 - 00:27.200 silence
00:27.200 - 00:37.200 sine wave (2 kHz, 0.0 dB FS peak)
00:37.200 - 00:40.200 silence

00:40.200 [check fall/rise time of peak meters]

00:40.200 - 00:42.200 sine wave (2 kHz, 0.0 dB FS peak)
00:42.200 - 00:44.200 silence

Validation settings
===================
File: meter_ballistics.flac
Host SR: 44 100 Hz
Channel: RMS: All, ITU-R: 1
Display: [x] Peak meter level
        [ ] True peak meter level
        [x] Average meter level
        [ ] Maximum peak level
        [ ] Max. true peak level
        [ ] Stereo meter value
        [ ] Phase correlation
Metering minima
===============
For the calculations, see the Python script “meter_ballistics.py”.

Fall time of average meters (sine wave, 0.0 dB FS peak)
=======================================================
99% of final reading in 600 ms integration time

Fall time average (K-20): -88.91 dB
Fall time average (K-14): -94.91 dB
Fall time average (K-12): -96.91 dB
Fall time average (Norm): -108.91 dB

Rise time of average meters (sine wave, 0.0 dB FS peak)
=======================================================
99% of final reading in 600 ms integration time

Rise time average (K-20): +18.90 dB
Rise time average (K-14): +12.90 dB
Rise time average (K-12): +10.90 dB
Rise time average (Norm): -1.10 dB

Fall time of peak meters (sine wave, 0.0 dB FS peak)
====================================================
-26 dB in 3 seconds

Fall time peaking (K-20): -6.00 dB
Fall time peaking (K-14): -12.00 dB
Fall time peaking (K-12): -14.00 dB
Fall time peaking (Norm): -26.00 dB

Rise time of peak meters (sine wave, 0.0 dB FS peak)
====================================================
immediate (one sample)

Rise time peaking (K-20): +20.00 dB
Rise time peaking (K-14): +14.00 dB
Rise time peaking (K-12): +12.00 dB
Rise time peaking (Norm): +0.00 dB