------------------------------------------------------------------------------

  This documentation and its accompanying audio file by Martin Zuther are
  licensed under a Creative Commons Attribution-ShareAlike 4.0 International
  License.

------------------------------------------------------------------------------

FLAC-compressed wave file (44.1 kHz, 24 bit, stereo)
====================================================
Please verify correctness of peak meter and maximum peak meter programmatically. In “ITU-R BS.1770” mode, make sure that measured levels equal the left channel's level.

Given levels describe the left channel. The left channel is delayed by one second, while the right channel's level has been attenuated by 1.93 dB.

00:00.000 - 00:02.000 silence
00:02.000 - 00:07.000 square wave ( 20 Hz, -41.0 dB FS peak)

        [left peak meter should read -21.00 dB (K-20)]
        [right peak meter should read -22.93 dB (K-20)]

        [left maximum peak should read -21.00 dB (K-20)]
        [right maximum peak should read -22.93 dB (K-20)]

00:07.000 - 00:09.000 silence
00:09.000 - 00:14.000 square wave ( 180 Hz, -29.0 dB FS peak)

        [left peak meter should read -9.00 dB (K-20)]
        [right peak meter should read -10.93 dB (K-20)]

        [left maximum peak should read -9.00 dB (K-20)]
        [right maximum peak should read -10.93 dB (K-20)]

00:14.000 - 00:16.000 silence
00:16.000 - 00:21.000 square wave ( 530 Hz, -17.5 dB FS peak)

        [left peak meter should read +2.50 dB (K-20)]
        [right peak meter should read +0.57 dB (K-20)]

        [left maximum peak should read +2.50 dB (K-20)]
        [right maximum peak should read +0.57 dB (K-20)]

00:21.000 - 00:23.000 silence
00:23.000 - 00:28.000 square wave (1111 Hz, -8.3 dB FS peak)

        [left peak meter should read +11.70 dB (K-20)]
        [right peak meter should read +9.77 dB (K-20)]

        [left maximum peak should read +11.70 dB (K-20)]
        [right maximum peak should read +9.77 dB (K-20)]

00:28.000 - 00:30.000 silence
00:30.000 - 00:35.000 square wave (1501 Hz, -0.1 dB FS peak)

        [left peak meter should read +19.90 dB (K-20)]
        [right peak meter should read +17.97 dB (K-20)]

        [left maximum peak should read +19.90 dB (K-20)]
        [right maximum peak should read +17.97 dB (K-20)]
00:35.000 - 00:37.000 silence
00:37.000 - 00:42.000 square wave (2890 Hz, -36.0 dB FS peak)

        [left peak meter should read -16.00 dB (K-20)]
        [right peak meter should read -17.93 dB (K-20)]

        [left maximum peak should read +19.90 dB (K-20)]
        [right maximum peak should read +17.97 dB (K-20)]

00:42.000 - 00:44.000 silence
00:44.000 - 00:49.000 square wave (4190 Hz, -69.5 dB FS peak)

        [left peak meter should read -49.50 dB (K-20)]
        [right peak meter should read -51.43 dB (K-20)]

        [left maximum peak should read +19.90 dB (K-20)]
        [right maximum peak should read +17.97 dB (K-20)]

00:49.000 - 00:51.000 silence
00:51.000 - 00:56.000 square wave (8345 Hz, -85.0 dB FS peak)

        (it seems like I have driven Sound Forge's test
        tone generator to its limits -- the peak level
        meter readings given below have been measured
        using the "Statistics" dialog in Sound Forge)

        [left peak meter should read -65.05 dB (K-20)]
        [right peak meter should read -66.99 dB (K-20)]

        [left maximum peak should read +19.90 dB (K-20)]
        [right maximum peak should read +17.97 dB (K-20)]

00:56.000 - 00:59.000 silence

Validation settings
===================
File: peak_meter.flac
Host SR: 44 100 Hz
Channel: RMS: All, ITU-R: 1
Display: [x] Peak meter level
        [ ] True peak meter level
        [ ] Average meter level
        [x] Maximum peak level
        [ ] Max. true peak level
        [ ] Stereo meter value
        [ ] Phase correlation