------------------------------------------------------------------------------

  This documentation and its accompanying audio file by Martin Zuther are
  licensed under a Creative Commons Attribution-ShareAlike 4.0 International
  License.

------------------------------------------------------------------------------

FLAC-compressed wave file (96 kHz, 24 bit, stereo)
==================================================
Please verify correctness of K-System meter values programmatically. In “RMS mode”, make sure that peak and average readouts match for sine waves.

Please notice that K-System meter readings may deviate from the true value at very low frequencies (fluctuations due to meter ballistics and audio chunk size) and very high frequencies (aliasing in the wave file).

00:00 - 00:03 silence
00:03 - 01:03 sine sweep (10 Hz to 48 kHz, -4.00 dB FS peak, logarithmic)

        [average meters should read +16.00 dB (K-20)]
        [peak meters should read +16.00 dB (K-20)]

01:03 - 01:06 silence
01:06 - 01:26 sine sweep (20 kHz to 24 kHz, -4.00 dB FS peak, linear)

01:11 [check peak meter for RMS filter cutoff @21 kHz]

01:26 - 01:29 silence
01:29 - 01:49 triangular sweep (20 Hz to 20 kHz, -4.00 dB FS peak, logarithmic)

        [average meters should read +14.24 dB (K-20)]
        [peak meters should read +16.00 dB (K-20)]

01:49 - 01:52 silence
01:52 - 02:12 square sweep (20 Hz to 20 kHz, -4.00 dB FS peak, logarithmic)

        [average meters should read +19.01 dB (K-20)]
        [peak meters should read +16.00 dB (K-20)]

02:12 - 02:15 silence

Validation settings
===================
File: rms_sweeps.flac
Host SR: 96 000 Hz
Channel: RMS: All, ITU-R: 1
Display: [x] Peak meter level
        [ ] True peak meter level
        [x] Average meter level
        [ ] Maximum peak level
        [ ] Max. true peak level
        [ ] Stereo meter value
        [ ] Phase correlation
RMS correction of K-System meter (sine wave, -4.00 dB FS peak)
==============================================================
RMS = A / sqrt(2)
RMS / A = sqrt(2) = +3.01 dB
+3.01 dB + (-4.00 dB) = -0.99 dB

K-20 = 20.00 dB + (-0.99 dB) = 19.01 dB
K-14 = 14.00 dB + (-0.99 dB) = 13.01 dB
K-12 = 12.00 dB + (-0.99 dB) = 11.01 dB
Norm = 0.00 dB + (-0.99 dB) = -0.99 dB

Sine wave (-4.00 dB FS peak)
============================
RMS = A / sqrt(2)
A / RMS = 1/sqrt(2) = -3.01 dB

K-20 = 19.01 dB + (-3.01 dB) = 16.00 dB
K-14 = 13.01 dB + (-3.01 dB) = 10.00 dB
K-12 = 11.01 dB + (-3.01 dB) = 8.00 dB
Norm = -0.99 dB + (-3.01 dB) = -4.00 dB

Triangular or sawtooth wave (-4.00 dB FS peak)
==============================================
RMS = A / sqrt(3)
A / RMS = 1/sqrt(3) = -4.77 dB

K-20 = 19.01 dB + (-4.77 dB) = 14.24 dB
K-14 = 13.01 dB + (-4.77 dB) = 8.24 dB
K-12 = 11.01 dB + (-4.77 dB) = 6.24 dB
Norm = -0.99 dB + (-4.77 dB) = -5.76 dB

Square wave (-4.00 dB FS peak)
==============================
RMS = A
A / RMS = 1 = 0.00 dB

K-20 = 19.01 dB + ( 0.00 dB) = 19.01 dB
K-14 = 13.01 dB + ( 0.00 dB) = 13.01 dB
K-12 = 11.01 dB + ( 0.00 dB) = 11.01 dB
Norm = -0.99 dB + ( 0.00 dB) = -0.99 dB